# Introduction, Terminology
## Terminology, definitions:
AGV	Automated Guided Vehicle
Host AGV	The AGV the Q-CAN is connected to
Contender AGV	The AGV that is a contender for the shared resource (FE/Door/Intersection ...)
Serial Port	All three port options: RS232, CAN, USB
RS232 Port	The specific port, RS-232
RF	Radio Frequency; in this context the QCAN2 radio subsystem
Serial Messages	Messages from the RS232 Serial Port or CAN bus or USB port
Commands	The Q-CAN radio and the vehicle computer communicate with several types of commands. A command is repeated as a series of messages until the desired reply is received.
Dispatcher	A computer system that can send work orders to a Q-CAN AGV when it is in a predefined zone and requesting dispatching.
Dispatching	Sequence of controls and commands used to send work orders to Q-CAN AGV.
Door (Bridge)	A place in the system where a vehicle needs to control, or interface with, fixed equipment in its path.
Intersections	Places in the system where vehicles cross each others path, and have the potential to collide.
Messages	There is a continuous flow of messages between the Q-CAN radio and the vehicle computer. If either unit stops sending messages the other will attempt to stop the vehicle.
Q-CAN	Quick Configurable AutomatioN mostly written as QCAN2
Q-CAN System	The collective of all Q-CAN devices on a single site.
Q-CAN Blocking	System Q-CAN Blocking System using small, limited range, radios to control AGV access to intersections.
Repeater	Radio Device for extending the useful range of the RF communications
Forwarder	Device / QCAN2 Mode to forward from RF to RS-232 and vice versa
Stations	Places in the system where the vehicle can stop to load or drop.
IDRD	Collective identifier for the the Intersection Controller, the Door Controller, the Repeater, and the Dispatch.
Door mechanism	The system that responds to door open commands including signaling door state.
XXX	Item not known or named at the time of writing.
IPPC	Intersection Pier to Pier Controller
CR	Central resource controller

## General Description
  Most of this chapter is a derivation from the original spec.
   The messages are carried between the AGV and QCAN2 via a serial port. In the QCAN2 the serial port could be RS232, CAN or USB. In the description below the numbers assumed to be are hexadecimal numbers, and the characters appear as they would in the ‘C’ language.
### The general format of the messages:
Meaning	Start Char	Message ID	Zone	Data_1	Data_2	Carriage Return	Notes
Typical Usage	/	Command	Zone Number	VID	Status	\r
Example1	/	01	10	03	00	\r	Send
Example2	/	81	10	03	00	\r	Recv

## Status Bit descriptions
  This is the format of data_2 field. It is used in many different contexts, so the meaning of the bit depends on which subsystem is in operation. Most of the bit allocation is identical to the previous specification version, except Bit_2; also for completeness, I included the switch bits.
  The status bits have changed from the original specification as per approval of Mr. Hinman. The progression of this particular bit field modifications: a.) Mar 4 2020; b.) Apr 9 2020; Changed as per recommendation from per Mr Hinman c.) Jun 01, 2020
## Bits, Authoritative as of Jun/02/2020:
Bit Number	Bit Value	Short Name (name in code)	Description
Bit_7	0x80	BLOCK_QCAN2	There is some other vehicle radio in the zone. AGV stops or slows based on context.
Bit_6	0x40	IN_CONTROL	The radio has uncontested control of the zone.
Bit_5	0x20	ERROR_QCAN2	Error Occurred; Missing Spec on error source
Bit_4	0x10	RELAY_BIT1	Set when Relay 2 is ON
Bit_3	0x08	BLOCK_FIXED	Fixed Equipment Blocking zone
Bit_2	0x04	RELAY_BIT0	Set when Relay 1 is ON
Bit_1	0x02	DOOR_BIT1	Fixed EQ input_1
Bit_0	0x01	DOOR_BIT2	Fixed EQ input_0

## Status code bit allocations (as updated)
Bit_7 (0x80) when set => Block (stop or slow / blocked)
Bit_6 (0x40) when set => This AGV is in control of the zone
Bit_5 (0x20) when set => Error occurred
Bit_4 (0x10) when set => No AGV occupies this zone
Bit_3 (0x08) when set => Fixed equipment occupied
Bit_2 (0x04) when set => No AGV present in the zone << NEW

Bit_1 (0x02) when set => Switch_1 active (FE context only)
Bit_0 (0x01) when set => Switch_0 active (FE context only)

 The rationale for bit_2 is to show if any AGV is in this zone either as an occupier or as a requester. This allows the AGV to see all that is present in the zone, which in turn allows for an informed choose on the part of the AGV for alternate route.

## QCAN2 BIT Allocation (jun/2020)

#define BLOCK_QCAN2	BIT_7
#define IN_CONTROL	BIT_6
#define ERROR_QCAN2	BIT_5
#define RELAY_BIT1	BIT_4
#define BLOCK_FIXED	BIT_3
#define RELAY_BIT0	BIT_2
#define DOOR_BIT1	BIT_1
#define DOOR_BIT0	BIT_0

# Serial Communications

AGV to QCAN2 and QCAN2 to AGV
  The data format is identical to the legacy QCAN. The command, Zone, Data_1, Data_2 are ASCII Hexadecimal characters, from 0-9 and A-Z. (Please note, in the current Savant serial com test suite, lowercase characters are not accepted)

Start	Command	Zone	Data_1	Data_2	Carriage Return
/	00-FF	01-FF	00-FF	00-FF	CR

  An example of communication string is:
/01237800\r
Which translates to command: 0x01 (anticipate) zone: 0x23 AGV: 0x78 parameter: 0x00

### Example: Open / Request Fixed Equipment:
  This is chapter is mostly a copy of the spec.
  The QCAN2 responds identically to these two commands, with the only difference in the response is the command received. 83 for command 03 and 84 for command 04. The QCAN2 always responds with the state of the two inputs on the fixed equipment controller regardless of whether or not the vehicle has control of the zone. The QCAN2 will
report the state of the two inputs in the STATUS byte, input 1 on STATUS bit 0 and input 2 on STATUS bit 1. The fixed equipment controller will assert output 1, and the vehicle QCAN2 will turn the BLOCKED bit in STATUS on or off to reflect the state of the fixed equipment controller's input 1 as well as the process of gaining control of the zone.
The 1.5 second priority resolution delay will apply to the STATUS BLOCKED bit response to input 1 the same as it does to becoming IN_CONTROL. That is, the vehicle QCAN2 can respond with the STATUS BLOCKED bit false (0) for 1.5 seconds, even if input 1 is false. After the 1.5 second priority resolution delay, the STATUS BLOCKED bit should be true (1) if either IN_CONTROL or input 1 is false.
  Q-CAN QCAN2 Specification Fixed equipment is permitted to ignore output 1 if the door or other fixed equipment is not supposed to be controlled by the vehicle. This could be a normally open door that we don't want the vehicle to run into if it is closed for some reason.
A fixed equipment QCAN2 is the Zone Controller. Since a vehicle could request control of the zone with the Request Zone command 02 before issuing these commands, and must not surrender control it has already gained, the fixed equipment controller must also monitor for this condition. Read Fixed Equipment (0A; 8A): The QCAN2 responds with the state of the two inputs on the fixed equipment controller regardless of whether or not the vehicle has control of the zone. The QCAN2 will report the state of the two inputs in the STATUS byte, input 1 on STATUS bit 0 and input 2 on STATUS bit 1. The state of those inputs will have no effect on the BLOCKED STATUS bit.
Once the vehicle is in control of the zone, fixed equipment controller output 1 will reflect STATUS bit 0 in the command, and output 2 will reflect STATUS bit 1. The outputs will only go active if explicitly commanded by the vehicle in control of the zone, and will be cleared when the vehicle turns them off or surrenders control of the zone. The "turn on output 1" implied in the Open / Request Fixed Equipment commands does not happen in response to this command. Likewise STATUS bits 4~7 returned by the QCAN2 reflect only the state of the requested zone, and are not affected by the state of the inputs on the fixed equipment controller.
  A fixed equipment QCAN2 is the Zone Controller. Since a vehicle could request control of the zone with the Request Zone command 02 before issuing this command, and must not surrender control it has already gained, the fixed equipment controller must also monitor for this condition.
Dispatcher Commands:
(detailed elsewhere)
# CAN BUS Communications

AGV to QCAN2 and QCAN2 to AGV
  The data format communicated over CAN is identical to the Serial RS-232 communications format. The max length of the CAN BUS message is 8 bytes, so the 10 byte QCAN2 message is transmitted in two frames; an 8 bytes frame and a 2 bytes frame.

### The CAN BUS parameters:
Parameter	Value
CAN Data Speed	250000
Data length	8 bytes + 2 bytes on next packet
**Transmit message ID (MSG_TID)	0x19EE5401
**Receive message ID (MSG_RID)	0x19EE5402

 ** Transmit / Receive as seen from the QCAN2’s point of view.

  Test and communication examples are provided for the commonly used ROBOTELL USB to CAN transceiver. (on the accompanying Jump Drive)

# Forwarders, Repeaters
    As mentioned in the earlier section, our new RF empowered us with new features. Every QCAN2 acts as a natural forwarder. If there is an RF starvation point, or long distance communication needing a repeater, placing a QCAN2 at that position should solve the problem.
## Repeater
  The repeater functions without any configuration changes. This relies on a subsystem we coined as the ‘mini network’. The mini network forwards the packets it sees, with an algorithm similar to how the internet works. Packets have a TTL (Time To Live) field, and this field is decremented every time the packet is forwarded. The packet is discarded if the TTL value reaches zero. Also, a packet has a Unique ID field, and packets that are seen before are not processed. This assures that a packet will travel to all destinations with the help of the intermediaries. One exception is the FE switch information. As it is updated without state change, the FE door switch information gets a unique ID every time it is updated.
## Forwarder
   The forwarder mode is a special mode for the QCAN2. It forwards packets arriving from the Radio Subsystem to the RS-232 port. These packets then can be transmitted via the serial port to another forwarder. The other Forwarder will broadcast the packet on the RF. This transmission is seamless, the RF packets forwarded rejoin the ‘mini network’. The mini network handles the forwarded packets with the same algorithm as the normal packets; the TTL field and Unique ID assures that a packet will propagate via air or wire. When the QCAN2 is in forwarder mode, the CPU LED will double blink.

 The forwarder mode can be configured on the main web page or on the command line. The command to toggle forward mode is: ‘forward’

This part of the page is left intentionally blank