# Controller Command Flow
(This whole section is implemented, no new information is added / needed)
## Intersection Controller Command Flow
 (Implemented, this section is informational)
   Included, a simplified table of intersection command flow. The rows are staggered, denoting the challenge and response structure of the communication. For full flow chart please see attached document titled: “Intersection Flowchart”.

  Keys: (ZZ=zone) (VV=Vehicle) (00-FF=Hex ASCII characters) (OPT=optional)

BIT_7 0x80 = BLOCKED	BIT_6 0x40 = IN_CONTROL
BIT_5 0x20 = ERROR	BIT_4 0x10 = RESOLVING

Spaces between fields are added for readability.

### AGV - QCAN2 Intersection Challenge / Response Table

AGV Sends	QCAN2 Responds	Status BITS	Condition/Comments
0x00 00 VV 00			Idle loop
	0x80 00 00 00		Idle loop response

0x01 ZZ VV 00			Anticipate Intersection (OPT)
	0x81 ZZ VV 00		Intersection is unoccupied
	0x81 ZZ 00 80	BIT_7	Intersection is occupied
	0x81 ZZ 00 A0/20	BIT_5 | ?	Radio Error

0x02 ZZ VV 00			Occupy Intersection
	0x82 ZZ VV 00		Intersection open
	0x82 ZZ VV FF	ALL	Intersection occupied (legacy)
	0x82 ZZ VV 10	BIT_4	Started resolving
	0x82 ZZ VV 90	BIT_7 | BIT_4	Preliminary NO
	0x82 ZZ VV 40	BIT_6	Intersection occupied by self
	0x82 ZZ VV 80	BIT_7	Intersection occupied by other
	0x82 ZZ VV C0	BIT_7 | BIT_6	Got Zone, but intersection occupied by other
	0x82 ZZ 00 20/A0/E0	BIT_5 | ?	Radio Error
0x00 ZZ VV 00			Release Intersection / ZZ VV fields are optional

0x00 00 VV 00			Idle loop
	0x80 00 VV 00		Idle loop

## Door Controller Command Flow

    Included, a simplified table of door controller command flow. The rows are staggered, denoting the challenge and response structure of the communication.

  Keys: (ZZ=zone) (VV=Vehicle) (00-FF=Hex ASCII characters) (OPT=optional) (SS=door status bits: Bit_0=input_1, Bit_1=input_2)

### AGV QCAN2 Door Challenge / Response Table

AGV Sends	QCAN2 Responds	Comments
0x00 00 00 00		Idle loop
	0x80 00 00 00	Idle loop
0x03ZZVV00		Anticipate (Open) Door (OPT)
	0x83 ZZ VV 00	Door zone is unoccupied
	0x83 ZZ VV FF	Door zone is occupied (AGV Slow)

0x04 ZZ VV 00		Door Request
	0x81 ZZ VV 00	Door zone is unoccupied
	0x81 ZZ VV FF	Door zone is occupied / (AGV Stop)

Open / Close Door	0x04 ZZ VV 81 – open / 0x04 ZZ VV 82 – close	Open / Close Door
		The 'Read fixed equipment' command can be used to poll the door status

0x0a ZZ VV 00		Read Fixed Equipment
	0x81 ZZ VV SS	Door status bits relayed
0x00 ZZ VV 00		Release Door and door Zone / ZZ VV optional
0x00 00 00 00		Idle loop
	0x80 00 00 00	Idle loop

## Dispatch Command Flow.

    Included, a simplified table of dispatch command flow. The rows are staggered, denoting the challenge and response structure of the communication. For full flow chart please see attached document titled: “Dispatch Flowchart” (under construction)
## Terminology:

Dispatch QCAN2	D-QCAN2	The QCAN2 that is attached to the dispatch computer.
AGV QCAN2	A-QCAN2	The QCAN2 that is attached to the AGV

 Table Keys: (ZZ=zone) (VV=Vehicle) (00-FF=Hex ASCII characters) (OPT=optional) (LL=Load Status: 01=Full FF=empty) (PP=Pick/Drop Command: 01=Pick, FF=Drop) (TT=Target / Destination Zone) (MM=Additional [More] Destinations: 00=Done, FF=More) ( ---- denotes state separation)

## AGV QCAN2 Dispatch Challenge / Response Table

AGV Sends	A-QCAN2 Responds to AGV	A-QCAN2 Sends to / D-QCAN2	D-QCAN2 Sends or Responds / to A-QCAN2	Comments
0x00 00 00 00
	0x80 00 00 00
0x05 ZZ VV LL				Awaiting Dispatch
		0x05 ZZ VV LL		Dispatch QCAN2 builds a table of available AGVS
-----	----	----	----	----
			0x07 TT 00 00	Anticipate Vehicle
	Relayed Unmodified
-----	----	----	----	----
			0x08 ZZ TT PP	Request Vehicle
		Relayed Unmodified		Dispatch QCAN2 responds from a table of available AGVS
	0x88 ZZ TT PP

0x06 ZZ VV TT / Accept Dispatch
		Relayed Unmodified
			0x09 ZZ VV TT	Confirm Vehicle
	0x89 ZZ VV TT
				Dispatch Complete
0x06 ZZ VV FF / Reject Dispatch
		Relayed Unmodified
			0x09 ZZ VV TT	Confirm Vehicle
	0x89 ZZ VV TT
				Dispatch Complete

# Fixed Equipment (DOOR) Relay Controls

Please Note:
  This section is obsolete, the development thread was created on the assumption that door controller needs a switch based priority resolution

   The formula for the door bit allocation is once a bit is occupied from one AGV, the other AGV(s) cannot reset it. Only after the first (and successive) AGV(s) release the door bit, it becomes possible to close it. This is to serve the intent, that once an AGV opened the door, it has exclusive control over releasing it.
Bit allocation table:
AGV_1 / Door Bit 0	AGV_1 / Door Bit 1	AGV_2 / Door Bit 0	AGV_2 / Door Bit 1		FE / Relay_1	FE / Relay_2
0	0	0	0		0	0
1	0	0	0		1	0
0	1	0	0		0	1
1	1	0	0		1	1

AGV_1 / Door Bit 0	AGV_1 / Door Bit 1	AGV_2 / Door Bit 0	AGV_2 / Door Bit 1		FE / Relay_1	FE / Relay_2
0	0	0	0		0	0
1	0	0	1		1	1
0	1	1	0		1	1
1	1	1	1		1	1

AGV_1 / Door Bit 0	AGV_1 / Door Bit 1	AGV_2 / Door Bit 0	AGV_2 / Door Bit 1		FE / Relay_1	FE / Relay_2
0	0	0	0		0	0
0	0	0	1		0	1
0	0	1	0		1	0
0	0	1	1		1	1

  Please note that in this table AGV_1 and AGV_2 are interchangeable, so the third (and forth) table are redundant.

  This bit table does not correspond to any standard (And / Or / Xor) table so we named it Central Resource Reset Protection table. (CRPT Table) Feedback needed / welcome.