# Fixed Equipment Controller / Door Controller
   The QCAN2 acts as a door controller if the FE zone number is set to a number between 1 - 255. The zone number 0 (zero) denotes that the QCAN2 is not in zone controller mode. This setting can be applied from the command line or the web interface. It is recommended to power cycle the QCAN2 after setting this mode. The mode and zone is stored in the QCAN2’s non volatile memory. The mode can be set any number of times, there is no limit.
   If there is another operating zone controller that is in radio range with the same zone number, the QCAN2 will blink the Red / Yellow / Green lights on off until the zone conflict is resolved.
  The QCAN2 Fixed Equipment controller facilitates communication between the AGV and a Fixed Equipment (Door Controller) mechanism. The AGV communicates with the FE controller (door controller) via the designated door commands. The QCAN2 door controller has four major function groups:

a.) Occupy Door Zone / Open Door
b.) Control the door (open / close relays)
c.) Report the status of the door.
d.) Leave Door Zone, Close door

   The commands correspond to functions of the door. a.) Open door b.) Close door.
  The status reports of the door correspond to: c.) Door in transition, Door opened, Door closed. The status of the door is passed back to the AGV for further action.
## Intersection controller and door controller combo
  When an AGV approaches an intersection, that is also a door, the command sequence is stacked. As the door is a singular resource, the intersection controller logic may be simplified. This intersection door combo may be deployed where the peer-to-peer intersection controller has difficulty. (Future Design Requirement)
## Door controller forwarding
   The Fixed Equipment controller will echo all commands to its RS-232 serial port, and will obey commands coming from said serial port. Attaching a serial cable to a QCAN2 forwarder’s RS-232 serial port will relay all Fixed Equipment commands in both directions. The forwarder can be placed strategically to solve RF starvation issues, for example controller behind steel door. There is also the possibility to place an RF forwarder without the use of cables.
# Fixed Equipment Flow Chart
  Below is a skeleton flowchart for the fixed equipment. It depicts the ideal flow, as the real life process is somewhat more complex. Over the evolution of the code the protocol changed, but the overall functionality stayed intact.

Exit FE Zone
Enter
Fixed FE Zone
AGV
Read Door
Message
EVAL
WAIT
IDLE
AGV
FE
Message
AGV
Release
Message

Notes:

1.) The Others?
Module consults the RF table
2.) The RELEASE Module issues specific release to the first contestant
\ 02 ZZ VV 00 → \ 82 ZZ VV 80
\ 00 00 00 00 → \ 80 00 00 00
\ 0a ZZ VV 00 → \ 8a ZZ VV 00
State Change
READ_DOOR

\ 03 ZZ VV 00 → \ 82 ZZ VV SS
Others?
No Yes
State Change
EVAL
State Change
RELEASE
State Change
BULLY

\ 00 00 VV 00 → \ 80 00 VV 00
Others?
No Yes

VV Vehicle
ZZ Zone
SS Status
Symbols:
Duplicate
Bully Handler

SW 1
No Yes

\ 04 ZZ VV 00 → \ 82 ZZ VV SS

WHATSUP

ISSUE
OPEN

Handled in QCAN2

## Fixed equipment timings
  This is a short description of the fixed equipment control protocol response timing. There are various timings for different sections.
- Switch state propagation
- Relay command propagation
- Relay state propagation
### Switch state propagation:
   From the change in switch state to the signal that arrives to the AGV QCAN2, the operation has several phases. 1.) Initiating switch status request; 2.) Broadcasting switch status; 3.) Injecting switch status request result to serial stream;
### Relay command propagation:
   From the relay change request to the signal that arrives to the FE QCAN2, the operation has several phases. 1.) Sending relay change request; 2.) Acting on the relay change request.
### Relay state propagation:
   From the change in relay state to the signal that arrives to the AGV QCAN2, the operation has several phases. 1.) Broadcasting relay status 2.) Injecting relay status result into the serial stream;
  Each phase in the above descriptions last a communication clock tick (appx. 300 ms each)
 The switch state propagation thus lasted 900 ms +- 2 ticks; This was deemed to be too long, so a caching mechanism is introduced. The SW state is broadcast on FE idle state, and the information is stored in a new table. (Much like the RF Table)
Background:
  The idle time keep alive packet now contains the SW state and Relay state. The information is cached in a separate table, and delivered on demand. The door table cache is updated on a one second periodicity, and expires in three seconds. By that time the regular door SW protocol delivers information, and the cache is discarded / ignored.
  SW Cache specification:
   Minimum latency 0 ms; max latency 1060 ms avg latency 530 ms for the broadcast.
(60 ms de-bounce + 1000 ms periodic update)
  Table size 32; oldest entry discarded if case of full table. The cache is applied to the stream immediately upon request.
  This allows the AGV QCAN2 to deliver immediate SW status response.
## General Timing parameters:
  The timing of the QCAN2 has constant elements, variable elements and random elements. This is due the fact, that actions concerning a common resource (like FE) need to be staggered in time. That way, the likelihood of competing occurrences / events is diminished.
  The QCAN2 state machine, in its simplified form consists of the following states:
State	Timing
QCAN_STATUS_IDLE	Indefinite**
QCAN_STATUS_EVAL	EVAL_TIME + rand( EVAL_TIME / 2)
QCAN_STATUS_BULLY / QCAN_STATUS_WAIT	Indefinite** / Decision based on other AGVs positions
QCAN_STATUS_RELEASE	RELE_TIME + rand(RELE_TIME / 2) or FE_RELE_TIME + rand(FE_RELE_TIME / 2)
QCAN_STATUS_IDLE	Indefinite** Loop back

Indefinite** No timing constraint, AGV signals the Beginning / End

  The states in the chart above cycle from the beginning to the end and loop back to the beginning. This simplified chart contains only the case state: “all is a go”, which we call the ‘YES ROUTE’. Timing for all other cases can be derived from the above graph.
#define EVAL_TIME 500 // How long to wait for bully resolution (ms)
#define RELE_TIME 500 // How long to pump IN release messages (ms)
#define FE_RELE_TIME 600 // How long to pump FE release messages (ms)
#define CR_RELE_TIME 600 // How long to pump CR release messages (ms)
#define REZ_RELE_TIME 800 // How long to pump release on abrupt zone (ms)
#define DUPBULLY_TIMER 300 // The time between two bully evaluations (ms)
#define WHATSUP_TIMER 300 // The time between two whatsup queries (ms)
## Summary of door controller timing:
  The switch status shows up in sub-second timing, the relay status shows up within 1 .. to .. 2 second delay. The relay command takes effect in 0.3 to 0.9 seconds.