# Repeater / Forwarder
  QCAN2 has an advanced packet forwarding mechanism. We coined the term 'mini network', because it operates on a similar principle as the internet. Packets are repeated from QCAN2 to QCAN2, until the time to live field reaches zero. This makes for a very efficient data transmission, and guarantees data will reach every single QCAN2 installation.

  The repeater will hold the signal that it receives, and repeats it. Three modes.

a.) Wired to Wireless
b.) Wireless to Wired
c.) Wireless to Wireless.

   By default the Wireless to Wireless repeater is always on. For most cases, placing a QCAN2 at the point of radio signal starvation should permit improved communication.

    The Mac address can also then be observed as the AGV number, (or a virtual zone number, or intersection number.) Because the QCAN2s communicate with each other based on this Mac address, zero configuration is automatic. The other major aspect of the configuration-less operation of the QCAN2, is that every control command is unique, and pertinent to a specific function, so the QCAN2 will always be able to distinguish what action to perform. One exception: the QCAN2 needs to be told it is a Wired to RF repeater. This can be done on the main page of the web configuration.

(This is addressed further in the door controller / intersection controller combo)