# Future development:
  The QCAN2 was implemented to legacy specifications. Technology has moved forward since the original specification, new tools, faster processors, modern RF and high speed communications have become available. This gives rise to a modernization opportunity to the QCAN2.
  In the following chapters we outline a specification proposal, based upon the learning acquired during the development of the QCAN2 device. It is not an error list, or defect list, it is a guide wire for a possible future direction in implementing QCAN3.
## The QCAN3 advancement
  The QCAN3 may move towards more real time interaction. The old device had a 400-500 ms serial transmission cycle, and the data was encapsulated within that packet. This was done with the intention of uniting the ‘stay alive’ and the ‘communication protocol’ messages.
  The new device would separate them into two distinctive streams: a.) stay alive and b.) data;
The stay alive could be shorter, for example 4 bytes. (CAN bus native length)
The data could be longer, for example 8 bytes;	(2 x CAN bus native length)
   The rational for the separation, is that the stay alive can function independently from the main data stream. This way the main data stream can be event driven; which allows faster response times. Also delivered content can be verified by an immediate return transmission.
   For instance the ‘stay alive could be delivered every 500 ms, 1000 ms being cause for timeout response. (2 missed packets)
  The data packet would contain information similar than the legacy devices, but the extra bytes would allow for a more consistent information flow. An example would be an additional op code for packet type identification. An op code for error conditions. A return packet could contain information about the reception / acknowledgment of the data, or the status of the operation itself.
  Avoiding the cementing of the details, here is a pseudo code that would achieve that:
PP=preable TT=type_code CC=command_code P1=param_1 P2=param_2 P3=param3 CS=checksum
     PP TT CC P1 P2 P3 CS
And the matching return code:
     PP TT CC R1 R2 R3 CS
  Assuming the preamble of 0xab, type code 0x01, here is how an occupy (02) zone 0x03 by AGV 0x45 would look like:
ab 01 02 03 45 00 00 CS
  The checksum could be any algorithm agreed to by both AGV and QCAN2; for example:

uint16_t sum_packet(const uint8_t *ptr, int len)
{
uint16_t sum = 0;	// Allow overflow
for(loop = 0; loop < len; loop++)
sum += ptr[aa];	// Per byte
return sum;
}
   The sum is checked by both peers, bad packets are discarded. The event is interpreted immediately, submitted to the QCAN3 state machine, and sent back as soon as data is available. This is different than the legacy device, it delivered information on the next round robin of the serial cycle.
  The RF can also be adapted to follow the semi real time model. Instead of following the round robin cycle of the incoming commands, one can deliver an immediate update to the RF subsystem, and accordingly, receive an immediate update.
  Events initialed by the QCAN3. The AGV is listening to async communications from the QCAN3 as well. External events like intersection events; door open events may reach the QCAN3 immediately.
## Centralized Intersection controller.
  The peer to peer intersection protocol theory has an inherent flow. The control is established peer to peer, relying on the participants to obey a controller peer. However, if the communication to the controller entity is severed, the other peers interpret it as a go signal. The resource relied on positive acknowledgment for negative action.
  The other theory is based upon the theory of a dedicated intersection controller. The resource is now controlled by a central resource controller, turning the cycle of positive acknowledgment to a positive action. If the communication to the central resource controller is severed, it is interpreted as a negative action, stopping the AGV. This assures that the AGV only goes if it has permission from the central resource controller, which results in a failure free theory of intersection controller. This theory can also be implemented in the QCAN2. The optimization is fail free theory vs. the additional cost of QCANX controllers.