# Intersection Controller
(Implemented, informational section only)
  Due to the dynamic nature of the intersections, QCAN2 will resolve AGV crossing priority via radio broadcast. In general, the resolution will proceed on a first-come first serve basis. QCAN2 and the AGV will go through several phases to coordinate intersection priority.

    The first phase is called 'anticipate intersection'. In this phase the QCAN2 will listen, and determine if there is a contesting AGV at the same intersection. If there is, the QCAN2 instructs the AGV to slow it's speed by transmitting on its serial port the OCCUPIED status, setting BIT_7

    The second phase is called 'request intersection'. At this point the QCAN2 will determine if the intersection is occupied. If intersection is occupied, the AGV will be instructed by the QCAN2 to stop, by transmitting on its serial port the OCCUPIED status BIT_7. Update: see new bit allocation at the end of this chapter. If the intersection is NOT occupied, the QCAN2 will continue to respond on the serial port to the ALIVE command, so the AGV will proceed.

   The third phase is called 'release intersection'. When the AGV reaches this phase, it instructs the QCAN2 to release this zone. The QCAN2 signals all other QCAN2s that the AGV cleared the intersection. Then, the other QCAN2s enter into an evaluation phase, and the AGV that has been waiting the longest, proceeds. (First come first served)
## Detailed Description of Messages:
 This is an augmented version of the specification, reflecting how the QCAN2 implemented the individual commands.
### Idle (0x00; 0x80):
The vehicle and QCAN2 exchanges this command and response pair when there is no task for the QCAN2 to do. This also serves a watchdog function, and the release function. The release function signals when the vehicle no longer wants to control a zone that the vehicle currently controls or is competing for. The idle function is awakened in other conditions like abrupt zone change or unexpected status change. TODO: to resolve ambiguities, separate functionality to distinct units. (release in particular)
### Watch Dog Stop (0xFF):
This message originates from the QCAN2. If and when the time gap between valid Serial messages are too long. The vehicle is responding with a full stop, and waits until new, meaningful message arrive.
### Anticipate Zone (01; 81):
A vehicle may send this command when it wants to know if another vehicle is in a zone without requesting control of that zone itself. This can be used by vehicle software to select an unoccupied route from among several possible routes to its destination. The QCAN2 will turn the BLOCKED bit in the STATUS byte on whenever it detects another vehicle competing for the zone, and off when no other QCAN2 is competing for or controling the zone. The QCAN2 may turn the BLOCKED bit on and off repeatedly as the presence or absence of other vehicles in the zone changes.
### Request Zone (0x02; 0x82):
  When a vehicle sends this command, it is requesting control of the zone. The QCAN2 will respond with one of the STATUS values described above under "Control of a Zone" to show where the vehicle QCAN2 is in the process of gaining control of the zone. Vehicle software will decide (possibly based on the QCAN2's default settings) how long the vehicle may continue to move without controlling the zone, to allow for priority resolution.

This part of the page is left intentionally blank
## Intersection Logic Chart

Exit Intersection
Enter
Intersection
AGV
Anticipate
Message
EVAL
WAIT
IDLE
IDLE
Loop
AGV
Request
Message
AGV
Release
Message
Others?
No Yes

Notes:

1.) The Others?
Module consults the RF table
2.) The RELEASE Module issues specific release to the first contestant
\ 02 ZZ VV 00 → \ 82 ZZ VV 80
\ 02 ZZ VV 00 → \ 82 ZZ VV 00
State Change
LISTEN

Others?
No Yes
State Change
EVAL

SLOW

State Change
RELEASE
State Change
BULLY

Others?
No Yes

VV Vehicle
ZZ Zone
SS Status
Symbols:

Duplicate
Bully Handler