# QCAN2 functional introduction
   This is a collection of notes produced during implementation. Comments are welcome. (Items that are marked ‘implemented’ are left there for informational purposes.) These implementation notes may also provide useful information on troubleshooting, and give an insight to the internal workings of the QCAN2. The document also contains notes that where exchanged between Savant and Akostar. If there is a conflict within the in contents, it is resolved by giving items marked ‘update’ priority.
  The previous title of this document was ‘Developer’s Manual’ which indicates its purpose and origin of contents within. Ideally, a ‘User Manual’ is derived from the contents of this document.
QCAN2 is the successor of QCAN, implemented with modern processors, and with powerful, updated RF technology. The device maintains connector and serial port compatibility, and similar command response to its predecessor. / Much like the legacy QCAN; this device implements several modes of operation. It will act as : / a.) Intersection controller, / b.) Fixed Equipment / Door controller, / c.) Intersection and/or door controller combo, / d.) Dispatch processor, and / e.) Command repeater or Communications Repeater. / In the QCAN2 we managed to resolve most - if not all - of the challenges of its precursor. For instance with modern processors we've got more memory, we can have more contenders at an intersection. We set this limit to 255, which is a reasonable compromise to allow us to allocate static buffers. / We have also been able to improve RF communication, using a peer to peer RF broadcast subsystem. This permitted every unit to act as a natural forwarder. The RF broadcast also enabled us to maintain RF state tables across devices, which is instrumental in determining vehicle priority. / With this new RF / CPU technology, we can use hardware features to create a queue of priorities on a first come first serve basis. This priority resolution is improved, as it is coordinated by the device's operating system (semaphore) functionality.

   We also added two powerful simulation software suites. One that is a successor of the QCANCom program, which sends commands to the QCAN2 serial port. The simulation then observes the QCAN2 responses.

  The other simulation is a Visual Modeling program, that simulates AGV action on screen. The on screen ‘virtual AGVs’ obey the QCAN2s instructions, much like its real counterpart. The simulation later got extended to loop out to a real RS-232 serial port. The responses are then interpreted. The on-screen AGV simulates the actions of the physical vehicle. The simulation accurately models the requirements of the AGV control. It has been an instrumental tool to create a Protocol and set of State Machine states that are immune to RF disturbances, and other anomalies. It also allowed us to visually troubleshoot resolution priorities.

   New tools are added. One can set up a QCAN2 to monitor all QCAN2s in range, see them in action, and optionally log the events as they happen. This is delivered as the utility called ‘AirMon’, and also installed on the laptop. The utility is developed in python, which lends itself to easy propagation into any other language. Here, one can visualize a monitoring tool delivered to the end user.

  This document contains some legacy descriptions. However, most chapters introduce new features, new utilities, new tools. This document also explains concepts related to implementation details. These new concepts arose empirically, during implementation. For example, the ‘Whatsup’ process allowed us to monitor every RF table in range, and create reports and error prevention actions based upon the collective content.
  Other sources of information:
- The original ‘Developer’s manual
- The QCAN2 debug command line help system
- The Web pages of the configuration screens