## WiFi Configuration Safety
   The WiFi password can be changed from the configuration page to prevent unauthorized access to the AGV configuration. From the same screen WiFi name can be changed, the WiFi name, as it appears on the air. The WiFi configuration times out after two minutes, so the configuration WiFi cannot be initiated after that time period. Pressing the QCAN2s on board button, or restarting the unit will activate the WiFi. If the WiFi password is lost, long pressing the on board button (12+s) will reset the Manufacturer's configuration. (The pass will reset to: 12345678)
### WiFi Device Compatibility
  The QCAN2 Configuration pages will operate in all common platforms and browsers. We tested PC / Apple / Unix / Android / Chrome Book devices, all of which showed complete compatibility. We tested Firefox / Chrome / Safari / Edge, and it showed visually identical page results.
## Zero Configuration Options
    The QCAN2 – wherever possible – has a zero configuration option. For example, the AGV sends its identity on most commands. The QCAN2 can decipher that, and store this as its host identity or target zone. The zero configuration options are possible because the command codes are function specific.
  The QCAN2 can distinguish all AGV actions sent to it, and bases its response upon it. On the RF side, the zero configuration is possible with the MAC address, as that is guaranteed to be globally unique.
### Zero Configuration Notes
  For safety, the QCAN2 will refuse to take on a second identity. (Obsolete: This function is only active in legacy mode.)
    In situations where the QCAN2 is connected to a different AGV than its original host, recovery is simple. Executing a long reset (hold QCAN2 button for 12+ seconds) on the QCAN2 will clear its memory, and it will be ready to adopt its new host. This way, on most instances, one can install a new QCAN2 without any tools or configuration just by simply plugging it in.
  Zero configuration does not apply to the door controller. The door zone has to be explicitly configured. Two methods of configuration: from the web interface, and the command line interface.
  On the web interface, on the main screen, set desired zone for the door, and press the “Save Configuration’ button.
  On the command line interface, the command ‘zone’ is available for setting the AGV’s own door zone. (An alias ‘doorzone’ is provided to verbalize the outcome better)
WARNING!
  The door zone has to be unique to the site. If more than one door controller is operating on the same zone, the radio will receive and feed information from both zone controllers. This is why the QCAN2 that detects a second zone controller on the same zone, will continuously blink all three ‘traffic’ lights. (Red/Yellow/Green)
   If there is a site door conflict, simply configure a different door zone. Alternatively, one may configure a different site code. However, when changing the site code, all QCAN2s have to be changed to that same site code. It is recommended to keep the default site code.