# Troubleshooting
The QCAN2 has many facilities to aid troubleshooting. Several distinct levels of diagnosis are available, from visual inspection of the LED s to looking at the serial communication to diagnosing the RF transmissions to connecting to the serial port. / 1.) Visual inspection of LED-s. / Perhaps the most telling LED is the RF reception LED. It blinks when there is an RF packet received. This confirms that there is another QCAN2 in range. / The blinking serial LED confirms the presence of the RS232 signal. If the QCAN2 is connected to the AGV via the CAN bus, the corresponding CAN LED should blink. / The CPU LED confirms the operation of the CPU. It blinks in a constant manner, roughly one per second. (exact timing detailed elsewhere) / The three LEDs titled ‘STOP’ / ‘EVAL’ / ‘GO’ describe the current state of the AGV control. Using the traffic light metaphor, the red color LED is for STOP AGV, the green one is for GO AGV. The yellow colored ‘EVAL’ is the ‘evaluate’ LED has multiple functions, and it represents a transitional state. On Anticipate, the yellow stands for full speed AGV, the yellow and red stands for slow speed AGV.

2.) Command Line Diagnostics
  This has been described extensively in the command line section.
3.) Hard Reset.
   Holding the QCAN2’s top button for 12+seconds will reset the QCAN to its original state, like it was configured by the manufacturer.
## Configuration error issues:
  The QCAN2 Is resilient against configuration difficulties. Only two configuration cases are detrimental.
### 1. Duplicate AGV IDs
This is not fatal, as this is only used in duplicate occupier resolution. If more than one AGV has the same ID, the resolution falls back to the MAC address. (which is globally unique) The Duplicate AGV IDs can be solved by detecting them at the dispatch level.
### 2. More than one FE (Door) controller on the same zone.
   When the QCAN2 powers up, it listens for the presence of a door controller on the same zone. If it detects a second door controller on the same zone, all the ‘traffic light’ LEDs flash, signaling zone conflict. (the ‘traffic light’ LEDs are the Red / Green / Yellow LEDs – Named STOP EVAL GO)
  The QCAN2 detects this condition on boot up, as the second FE can detect if there is already a FE within the same zone. This way the error could be signaled early, to prevent the two controllers from mixing up communication and interfering with one another. The two FEs on the same zone can deliver conflicting information, the symptom of which is intermittent switch state indications.
## Diagnostic Charts:
The following charts can be used to run the diagnoses.

This part of the page is intentionally left blank.
## General Troubleshooter:

Start
Troubleshoot
Power issue
Power LED?
Yes
No

5V LED?
12V LED?
CPU LED
Blinking?
Power LED?
Yes
No

Remit to
Servicing

No

RF LED
Blinking?

Other
QCAN2
Nearby?
Yes
Yes
Serial
 LED
Blinking?

No
Serial
Troubleshooter

RF
Troubleshooter

Logic
Troubleshooter

Yes
No
Yes
No

## RF Troubleshooter:

RF
Troubleshooter

Antenna
Connected?
No
Yes
LED
Operational?
No
Yes
Connect / Replace
Antenna

This stage assumes
two QCAN2s
In proximity

Remit for
Service

QCAN2
Operational

QCAN2 on
RF monitor?

Yes
No
Receiver Dead
Transmitter
Failure

## Logic Troubleshooter
  The QCAN2 has an self test function built in. After activating the self test, the QCAN2 cycles between intersection states in 5 sec to 15 sec interval. The self test zone is 100 (decimal). By activating the self test on more than one QCAN2, it is observable that they obey each other’s occupy stages. To activate the self test, press the QCAN2 button four times in succession. (Like a mouse double click, but four clicks) The LEDs indicate as the device cycles.

Logic
Troubleshooter
Traffic
Sequence
OK?
QCAN2 will run
Intersection
Self test
QUAD press
(4 times) Top
Button

Yes
No
Remit for
Service
QCAN2
Operational